Lecture Notes 9/9/2009:  Z-1 of Rational Functions and Sampling

Inverting Rational Z-Functions

- Rational X(z) are very important in signal processing

  - Example:  , where P(z) and Q(z) are polynomials

- Steps to invert…

    - Factor the numerator and denominator… , where a is a constant.

    - Partial fraction expansion

    - Use geometric series to expand

    - Obtain x[n] by comparison with

- Observe…

  - can be recovered (up to a constant multiplier) from its zeros and poles.

  - Example:

X(z):  	Two zeros @ z1 = j, z2 = 4

Three poles @ p1 = 2j, p2 = 3, p3 = 5

Noting:

Sampling

- Sampling enables the conversion from analog to digital

sample		       sample

Analog Signal     (	DT Signal    (    Digital Signal

- How to sample…

  - Simple scheme for sampling an analog signal

T – period sampling

τ – length of interval during which switch is closed

τ/T – duty cycle

Note:

- Fourier Analysis of Sampling

  - Note:  Trick –

  - Ideal Case

τ ( 0… better known as delta-functions

for all k’s

# Text boxes

z

0-

pole

x(t)

1/τ

xs(t)